PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

To reach the tidal bench marks, from Hilo Airport proceed out to the airport

exit to Kanoelehua Avenue (Route 11) and turn right, proceed 1.1 km (0.7 mi) to

Kamehameha Highway (Route 19) and turn right, bear NE onto Kalanianaole Street

and proceed 1.1 km (0.7 mi) to Kuhio Street leading into the Port of Hilo, turn

left onto Kuhio Street, pass through the gate into the Port of Hilo and bear NW

to Pier 2.  The bench marks are located along SR11 and are in the vicinity of

Pier 2.  The tide station is a wooden building inside the Pier 2 warehouse.

T I D A L   B E N C H   M A R K S

PRIMARY BENCH MARK STAMPING:  NO 4 1951

DESIGNATION:          161 7760 TIDAL 4

MONUMENTATION:           Tidal Station disk                        VM#:     1663

AGENCY:                  US Coast and Geodetic Survey (USC&GS)     PID#:  TU0020

SETTING CLASSIFICATION:  Concrete foundation

The primary bench mark is a disk set in top of east corner of the northern-most

concrete foundation for elevated water tank which rests on solid rock on State

Port of Hilo property, about 146 m (480 ft) south of the foot of Pier 1, and 58

m (189 ft) west of the centerline of the main gate.

BENCH MARK STAMPING:  PIER 3

DESIGNATION:          161 7760 PIER 3

MONUMENTATION:           Triangulation Station disk                VM#:     1662

AGENCY:                  U.S. Army Corps of Engineers (USCOE)      PID#:  TU0023

SETTING CLASSIFICATION:  Concrete pier deck

The bench mark is a disk set flush in concrete deck of Pier 2 and 3, about 6 m

(20 ft) from the west end of pier, 2.99 m (9.8 ft) NE of SW face of Pier 3, and

2.59 m (8.5 ft) south from north face of Pier 2.

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Page  2 of  8

PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

T I D A L   B E N C H   M A R K S

BENCH MARK STAMPING:  E 2 1926

DESIGNATION:          161 7760 E 2

MONUMENTATION:           Tidal Station disk                        VM#:     1665

AGENCY:                  US Coast and Geodetic Survey (USC&GS)     PID#:  TU0017

SETTING CLASSIFICATION:  Concrete pier deck

The bench mark is a disk set in the concrete deck at the southern end of Pier 1,

12.50 m (41.0 ft) NW of the SW corner of the Pier 1 building, 3.05 m (10.0 ft)

south of the pier face corner, 0.76 m (2.5 ft) west of the southern-most bollard

along Pier 1, and 0.09 m (0.3 ft) below level of asphalt.

BENCH MARK STAMPING:  F

DESIGNATION:          161 7760 F

ALIAS:                USE (F 1965)

MONUMENTATION:           Triangulation Station disk                VM#:     1666

AGENCY:                  U.S. Army Corps of Engineers (USCOE)      PID#:  TU0022

SETTING CLASSIFICATION:  Concrete pier deck

The bench mark is a disk set flush in concrete deck of Pier 3, 45.57 m (149.5

ft) NW of the SE (inshore) end of Pier 3, 30.18 m (99.0 ft) NW of bench mark 161

7760 TIDAL 5, 0.30 m (1.0 ft) SW of a 0.76 m x 1.22 m (2.5 ft x 4 ft) steel

cover plate flush with the pier, and 0.30 (1.0 ft) NE of SW face of pier.

BENCH MARK STAMPING:

DESIGNATION:          161 7760 TIDAL 5

ALIAS:                5 1959

MONUMENTATION:           Triangulation Station disk                VM#:     1667

AGENCY:                  U.S. Army Corps of Engineers (USCOE)      PID:

SETTING CLASSIFICATION:  Concrete pier deck

The bench mark is a disk set flush in concrete deck of Pier 3, 15.39 m (50.5 ft)

NW of the SE (inshore) end of Pier 3, and 0.30 m (1.0 ft) NE of SW face of pier.

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Page  3 of  8

PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

T I D A L   B E N C H   M A R K S

BENCH MARK STAMPING:  7760 A 1983

DESIGNATION:          161 7760 A

MONUMENTATION:           Tidal Station disk                        VM#:     1670

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Rock outcrop

The bench mark is a disk set in a lava rock outcropping in the south corner of

the U.S. Customs yard at the intersection of Kalanianole and Kuhio Streets,

28.56 m (93.7 ft) SW of the SW corner of the U.S. Customs House, 16.06 m (52.7

ft) SW of the west leg of a 15 m (50 ft) micro wave antenna, 4.27 m (14.0 ft)

west of the west edge of a driveway that leads to the U.S. Customs Parking Lot,

1.92 m (6.3 ft) east of a chain fence that surrounds the Armour Oil Hawaii Tank

Farm, and  0.09 m (0.3 ft) above ground level.

BENCH MARK STAMPING:  7760 B 1983

DESIGNATION:          161 7760 B

MONUMENTATION:           Tidal Station disk                        VM#:     1671

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Concrete slab

The bench mark is a disk set on the most northerly corner of a 2 m x 1.37 m (8

ft x 4.5 ft) platform that supports two large green telephone relay boxes under

a roof on the west side of a driveway that leads to the green warehouse at 888

Kalanianaole Street, 92 m (302 ft) SW of bench mark 7760 C 1983, 24 m (80 ft) NW

of the most westerly corner of the warehouse, 10.76 m (35.3 ft) SE of the

centerline of Kalanianaole Street, and 4.42 m (14.5 ft) SE of a utility pole.

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Page  4 of  8

PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

T I D A L   B E N C H   M A R K S

BENCH MARK STAMPING:  7760 C 1983

DESIGNATION:          161 7760 C

MONUMENTATION:           Tidal Station disk                        VM#:     1672

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Rock outcrop

The bench mark is a disk set in a lava outcropping on the south side of

Kalanianole Street betweet telephone poles Nos. 33 and 34, about 0.3 km (0.2 mi)

NE along Kalanianole Street from the U.S. Customs House on Kuhio Street, 92 m

(302 ft) NE of bench mark 7760 B 1983, 22.68 m (74.4 ft) east of a yellow fire

hydrant, 16 m (54 ft) east of utility pole #33, 12.65 m (41.5 ft) SW of

telephone pole #34, 12.04 m (39.5 ft) south of the centerline of Kalanianole

Street, 0.15 m (0.5 ft) south of the edge of the outcropping, and 1.07 m (3.5

ft) above ground level.

BENCH MARK STAMPING:  7760 G 1987

DESIGNATION:          161 7760 G

MONUMENTATION:           Tidal Station disk                        VM#:     1673

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Lava rock outcrop

The bench mark is a disk set in a lava outcropping fronting SS Motor Supply at

500 Kalanianaole Street across street from grey ware house, 27.74 m (91.0 ft) SW

of old utility pole #17X, 24.38 m (80.0 ft) NE of a yellow fire hydrant, 6.89 m

(22.6 ft) north of NW corner of a white metal faced building, 4.21 m (13.8 ft)

NW of NW face of building, 1.40 m (4.6 ft) SE of edge of road, and 0.46 m (1.5

ft) above road level.

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Page  5 of  8

PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

T I D A L   B E N C H   M A R K S

BENCH MARK STAMPING:  LYMAN 1977

DESIGNATION:          161 7760 LYMAN

MONUMENTATION:           Horizontal Station disk                   VM#:     1757

AGENCY:                  National Geodetic Survey (NGS)            PID#:  TU2250

SETTING CLASSIFICATION:  Concrete monument in pavement

The bench mark is a disk set in a 0.3 m (1 ft) square concrete monument on the

east side of the curving intersection of Silva and Kamehameha Roads, 13.26 m

(43.5 ft) east of the centerline of the road, 7.47 m (24.5 ft) east of the guard

rail, 2.53 m (8.3 ft) west of the corner of a cyclone fence bordering the west

side of Hilo Airport, and at road level.

BENCH MARK STAMPING:  LYMAN NO 2 1977

DESIGNATION:          161 7760 LYMAN NO 2

MONUMENTATION:           Reference Mark disk                       VM#:     1758

AGENCY:                  National Geodetic Survey (NGS)            PID#:  AA3569

SETTING CLASSIFICATION:  Lava rock outcrop

The bench mark is a disk set in a flat lava outcrop on the west side of the

curving intersection of Silva and Kamehameha Roads, about 91 m (300 ft) north of

a large orange wind sock on the west side of Hilo Airport, 24.11 m (79.1 ft) NW

of bench mark LYMAN 1977, 10.85 m (35.6 ft) west of the centerline of the road,

and slightly above grade.

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Page  6 of  8

PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

T I D A L   B E N C H   M A R K S

BENCH MARK STAMPING:  7760 H 1994

DESIGNATION:          161 7760 H

MONUMENTATION:           Tidal Station disk                        VM#:    12706

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Concrete pier deck

The bench mark is a disk set in the concrete deck of Pier 2 Port of Hilo, 81.32

m (266.8 ft) east of the west end of Pier 2/3, 29.05 m (95.3 ft) east of the 135

degree corner where Pier 2 face changes from a northerly to a northwesterly

direction, 18.75 m (61.5 ft) NW of the NW corner of Pier 2/3 transit shed, 8.90

m (29.2 ft) NE of a red fire plug, 0.94 m (3.1 ft) south of the face of Pier 2,

and 0.61 m (2.0 ft) SW of the center of a 0.30 m (1.0 ft) high steel bollard.

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Page  7 of  8

PUBLICATION DATE:  08/23/2000

Station ID: 1617760                                SUPERCEDED DATE:   04/21/2003

Name:       HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND

HAWAII

NOAA Chart: 19324                                  Latitude:         19° 43.8' N

USGS Quad:  HILO                                   Longitude:       155°  3.4' W

T I D A L   D A T U M S

Tidal datums at HILO, HILO BAY, KUHIO BAY, HAWAII ISLAND based on:

LENGTH OF SERIES:      18 YEARS

TIME PERIOD:           January 1976 - December 1993

TIDAL EPOCH:           1960-1978

CONTROL TIDE STATION:  1612340 HONOLULU, HONOLULU HARBOR, OAHU ISLAND

Elevations of tidal datums referred to Mean Lower Low Water (MLLW), in METERS:

HIGHEST OBSERVED WATER LEVEL (01/20/1981)    =  1.192

MEAN HIGHER HIGH WATER (MHHW)                =  0.756

MEAN HIGH WATER (MHW)                        =  0.619

MEAN SEA LEVEL (MSL)                         =  0.363

MEAN TIDE LEVEL (MTL)                        =  0.357

MEAN LOW WATER (MLW)                         =  0.098

MEAN LOWER LOW WATER (MLLW)                  =  0.000

LOWEST  OBSERVED WATER LEVEL (06/20/1955)    = -0.451

National Geodetic Vertical Datum (NGVD 29)

Bench Mark Elevation Information           In METERS above:

Stamping or Designation       MLLW      MHW  MLLW-MSL  MSL

NO 4 1951                     3.511    2.892   0.363   3.148

PIER 3                        2.776    2.157   0.363

E 2 1926                      2.563    1.944   0.363

F                             2.747    2.129   0.363

161 7760 TIDAL 5              2.748    2.129   0.363

7760 A 1983                   5.945    5.326   0.363

7760 B 1983                   4.559    3.940   0.363

7760 C 1983                   5.889    5.271   0.363

7760 G 1987                   5.944    5.325

LYMAN 1977                    8.463    7.844

LYMAN NO 2 1977               8.368    7.750

7760 H 1994                   2.762    2.143

The PIDs below are tidal benchmarks, but do not have all the necessary information required to create an image of the tidal and orthometric heights.
PID Latitude Longitude
AA3569 N194332 W1550327
TU0025 N194332 W1550400
TU2250 N194332 W1550326
TU0020 N194354 W1550324
TU0022 N194357 W1550329
TU0017 N194358 W1550326
TU0018 N194358 W1550326
TU0023 N194359 W1550333
TU0016 N194409 W1550325
TU0015 N194410 W1550325