U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Station ID: 1611347                                PUBLICATION DATE:  04/21/2003

Name:       PORT ALLEN, HANAPEPE BAY, KAUAI ISLAND

HAWAII

NOAA Chart: 19382                                  Latitude:         21° 54.2' N

USGS Quad:  HANAPEPE                               Longitude:       159° 35.5' W

Port Allen, Hanapepe Bay, Kauai Island ,

Station ID: 1611347

To reach the tidal bench marks from the airport in Kauai, turn left on to

Highway 50 (west) and continue on Highway 50 for approximately 8 km (5 mi) until

you reach Port Allen.  At Port Allen, turn left on Highway 541 and go about 1.2

km (0.7 mi) to  the State of Hawaii transit building on the pier.  The gauge was

located inside the building and the bench marks are located in the vicinity.

Oct 24 2006 19:47        ELEVATIONS ON STATION DATUM

National Ocean Service (NOAA)

Station:  1611347                                           T.M.:         0 W

Name:     PORT ALLEN, HANAPEPE BAY, KAUAI ISLAND, HI        Units:       Feet

Status:   Accepted                                          Epoch:  1983-2001

Datum         Value  Description

---------  --------  --------------------------------------

MHHW           5.16  Mean Higher-High Water

MHW            4.76  Mean High Water

DTL            4.24  Mean Diurnal Tide Level

MTL            4.13  Mean Tide Level

MSL            4.15  Mean Sea Level

MLW            3.51  Mean Low Water

MLLW           3.32  Mean Lower-Low Water

GT             1.84  Great Diurnal Range

MN             1.24  Mean Range of Tide

DHQ            0.40  Mean Diurnal High Water Inequality

DLQ            0.20  Mean Diurnal Low  Water Inequality

HWI            1.49  Greenwich High Water Interval (in Hours)

LWI            7.80  Greenwich Low  Water Interval (in Hours)

NAVD                 North American Vertical Datum

Maximum        9.13  Highest Water Level on Station Datum

Max Date   19920912  Date Of Highest Water Level

Max Time      01:18  Time Of Highest Water Level

Minimum        2.40  Lowest  Water Level on Station Datum

Min Date   19910514  Date Of Lowest Water Level

Min Time      18:54  Time Of Lowest Water Level

T I D A L   D A T U M S

Tidal datums at PORT ALLEN, HANAPEPE BAY, KAUAI ISLAND based on:

LENGTH OF SERIES:      7 Years

TIME PERIOD:           January 1990 - December 1996

TIDAL EPOCH:           1983-2001

CONTROL TIDE STATION:  1611400 NAWILIWILI, NAWILIWILI HARBOR, KAUAI

Elevations of tidal datums referred to Mean Lower Low Water (MLLW), in METERS:

HIGHEST OBSERVED WATER LEVEL (09/12/1992)    =  1.772

MEAN HIGHER HIGH WATER (MHHW)                =  0.561

MEAN HIGH WATER (MHW)                        =  0.439

MEAN SEA LEVEL (MSL)                         =  0.254

MEAN TIDE LEVEL (MTL)                        =  0.249

MEAN LOW WATER (MLW)                         =  0.060

MEAN LOWER LOW WATER (MLLW)                  =  0.000

LOWEST  OBSERVED WATER LEVEL (05/14/1991)    = -0.279

National Geodetic Vertical Datum (NGVD 29)

Bench Mark Elevation Information           In METERS above:

Stamping or Designation               MLLW        MHW

1347 A 1988                            3.421    2.982

1 1926                                 4.328    3.889

3 1926                                 9.638    9.199

35                                    10.644   10.205

1347 B 1988                            3.285    2.846

1347 C 1988                            7.020    6.581

1347 D 1988                           10.542   10.103

1347 E 1991                            2.103    1.664

1347 F 1991                           10.883   10.444

PIER STATION PIER 7 1981               3.342    2.903

T I D A L   B E N C H   M A R K S

PRIMARY BENCH MARK STAMPING:  1347 A 1988

DESIGNATION:          161 1347 A

MONUMENTATION:           Tidal Station disk                        VM#:    12294

AGENCY:                  National Ocean Survey (NOS)               PID:

SETTING CLASSIFICATION:  Concrete pier

The primary benck mark is a disk set between two 6-inch diameter red steel posts

that stand 1.52 m (5.0 ft) high and protect an emergency fire pump station, 2.74

m (9.0 ft) east of the large roll-up main entrance door of the State of Hawaii

Port Allen transit shed, and 1.25 m (4.1 ft) NE of a 10-inch diameter hole cut

through the pier deck which has a steel 8-inch pipe through it.

BENCH MARK STAMPING:  1 1926

DESIGNATION:          161 1347 TIDAL 1

MONUMENTATION:           Tidal Station disk                        VM#:     6449

AGENCY:                  US Coast and Geodetic Survey (USC&GS)     PID:

SETTING CLASSIFICATION:  Concrete foundation

The bench mark is a disk set in a concrete foundation for a derrick on an

abandoned loading wharf at the SW end of Eleele, near the inshore end on the NW

side of breakwater, at the east side of Hanapepe Bay, 122 m (400 ft) SE across

the water from present Port Allen Pier, 41 m (135 ft) SW of a stairway leading

up to the top of a small bluff, 29 m (96 ft) SW of inshore end of pier, 6 m (20

ft) SW of an old engine hoist, 1.22 m (4.0 ft) NW of a concrete stairway leading

down to a lower level boat landing, 0.40 m (1.3 ft) SW of the edge of

foundation, and 0.21 m (0.7 ft) above the wharf level.

BENCH MARK STAMPING:  3 1926

DESIGNATION:          161 1347 TIDAL 3

MONUMENTATION:           Tidal Station disk                        VM#:     6450

AGENCY:                  US Coast and Geodetic Survey (USC&GS)     PID:

SETTING CLASSIFICATION:  Concrete slab

The benck mark is a disk set in a concrete cornerstone at the west end of the

ruins of a warehouse foundation wall, on a bluff above the inshore end of

breakwater, 82.30 m (270.0 ft) WSW of gas storage tanks, on the north edge of a

cut through which railway passed, 5.94 m (19.5 ft) SE of a power pole, 4.11 m

(13.5 ft) east of a top step of a stairway leading down to an old wharf, 0.46 m

(1.5 ft) west of a wall foundation, and 0.91 m (3.0 ft) below the top of

foundation.

BENCH MARK STAMPING:  35

DESIGNATION:          161 1347 TIDAL 35

ALIAS:                4

MONUMENTATION:           Bench Mark disk                           VM#:     6451

AGENCY:                  US Geological Survey (USGS)               PID:

SETTING CLASSIFICATION:  Concrete monument

The benck mark is a disk set in a 0.3 m (1 ft) diameter truncated concrete cone

extending 0.3 m (1 ft) above a 0.91 m (3.0 ft) diameter base on a bluff at the

inshore end of breakwater, 82.30 m (270.0 ft) WSW of gas storage tanks,  9.60 m

(31.5 ft) north of bench mark 3 1926, 8.23 m (27.0 ft) ENE of power pole #9902,

4.57 m (15.0 ft) WNW of a right angle bend in gas mains, 3.81 m (12.5 ft) west

of west one of a row of seven gas mains, and 0.21 m (0.7 ft) above the ground.

BENCH MARK STAMPING:  1347 B 1988

DESIGNATION:          161 1347 B

MONUMENTATION:           Tidal Station disk                        VM#:    12295

AGENCY:                  National Ocean Survey (NOS)               PID#:  AA3584

SETTING CLASSIFICATION:  Concrete pier

The benck mark is a disk set 29.84 m (97.9 ft) NW of the southerly edge of the

pier, 20.12 m (66.0 ft) SW of a fire hydrant, 0.79 m (2.6 ft) south of the

center of a steel bollard at the NE inshore end of pier, and 0.79 m (2.6 ft)

east of the NE corner of the pier transit shed.

BENCH MARK STAMPING:  1347 C 1988

DESIGNATION:          161 1347 C

MONUMENTATION:           Tidal Station disk                        VM#:    12296

AGENCY:                  National Ocean Survey (NOS)               PID:

SETTING CLASSIFICATION:  Concrete slab

The benck mark is a disk set 11 m (36 ft) NW of the centerline of State Highway

541 where it terminates at the dock, 10.39 m (34.1 ft) SW of utility pole #9,

4.02 m (13.2 ft) south of the center of the steel pump housing, and 0.15 m (0.5

ft) from the southerly corner of a 3 m x 6 m (10 ft x 20 ft) concrete slab of a

sewage pumping station,

BENCH MARK STAMPING:  1347 D 1988

DESIGNATION:          161 1347 D

MONUMENTATION:           Tidal Station disk                        VM#:    12297

AGENCY:                  National Ocean Survey (NOS)               PID:

SETTING CLASSIFICATION:  Concrete foundation

The benck mark is a disk set at the NE corner of an unused 15 m x 69 m (50 ft x

225 ft) concrete foundation of former fish tank, 30.57 m (100.3 ft) SW of edge

of a macadam road, 19.42 m (63.7 ft) SE of the centerline of State Highway 541,

11.58 m (38.0 ft) NW of the NW corner of a large aluminum sided commercial

building, and 0.76 m (2.5 ft) above ground level.

BENCH MARK STAMPING:  1347 E 1991

DESIGNATION:          161 1347 E

MONUMENTATION:           Tidal Station disk                        VM#:    12403

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Concrete jetty foundation

The benck mark is a disk set in a concrete foundation at the south end of a

small concrete jetty, 22.25 m (73.0 ft) south of a light foundation on the

jetty, 0.70 m (2.3 ft) from the north edge of the foundation, 0.27 m (0.9 ft)

from the east edge of the foundation, and  0.70 m (2.3 ft) above the ground.

BENCH MARK STAMPING:  1347 F 1991

DESIGNATION:          161 1347 F

MONUMENTATION:           Tidal Station disk                        VM#:    12404

AGENCY:                  National Ocean Service (NOS)              PID:

SETTING CLASSIFICATION:  Concrete ramp

The benck mark is a disk set in a concrete ramp in the middle of a warehouse on

the NW side of Waialo Road, located on the west corner of a ramp leading to Car

Crafts at 4341 Waialo Road (located in the middle of the building flanked by C&S

Feed and Supply to the NE and Martin Steel Constructors, Inc. to the SW), 0.30 m

(1 ft) from the building, 0.21 m (0.7 ft) from the SW edge of the ramp, and 0.37

m (1.2 ft) above ground.

BENCH MARK STAMPING:  PIER STATION PIER 7 1981

DESIGNATION:          161 1347 PIER LANI 7

MONUMENTATION:           Bench Mark disk                           VM#:    12405

AGENCY:                  US Army Corps of Engineers (USE)          PID:

SETTING CLASSIFICATION:  Concrete pier deck

The benck mark is a disk set near the westerly corner of the Port Allen pier,

8.26 m (27.1 ft) SE of the westerly corner, 2.74 m (9.0 ft) SW of the westerly

corner of a transit shed, and 1.22 m (4.0 ft) NE of the SW edge of the pier.

D E F I N I T I O N S

Mean Sea Level (MSL) is a tidal datum determined over a 19-year National Tidal

Datum Epoch.  It pertains to local mean sea level and should not be confused

with the fixed datums of North American Vertical Datum of 1988 (NAVD 88).

NGVD 29 is a fixed datum adopted as a national standard geodetic reference for

heights but is now considered superseded.  NGVD 29 is sometimes referred to as

Sea Level Datum of 1929 or as Mean Sea Level on some early issues of Geological

Survey Topographic Quads.  NGVD 29 was originally derived from a general

adjustment of the first-order leveling networks of the U.S. and Canada after

holding mean sea level observed at 26 long term tide stations as fixed.

Numerous local and wide-spread adjustments have been made since establishment in

1929.  Bench mark elevations relative to NGVD 29 are available from the National

Geodetic Survey (NGS) data base via the World Wide Web at

National Geodetic Survey.

NAVD 88 is a fixed datum derived from a simultaneous, least squares, minimum

constraint adjustment of Canadian/Mexican/United States leveling observations.

Local mean sea level observed at Father Point/Rimouski, Canada was held fixed as

the single initial constraint.  NAVD 88 replaces NGVD 29 as the national

standard geodetic reference for heights.  Bench mark elevations relative to

NAVD 88 are available from NGS through the World Wide Web at

National Geodetic Survey.

NGVD 29 and NAVD 88 are fixed geodetic datums whose elevation relationships to

local MSL and other tidal datums may not be consistent from one location to

another.

The Vertical Mark Number (VM#) and PID# shown on the bench mark sheet are unique

identifiers for bench marks in the tidal and geodetic databases, respectively.

Each bench mark in either database has a single, unique VM# and/or PID# assigned.

Where both VM# and PID# are indicated, both tidal and geodetic elevations are

available for the bench mark listed.

The NAVD 88 elevation is shown on the Elevations of Tidal Datums Table Referred

to MLLW only when two or more of the bench marks listed have NAVD 88 elevations.

The NAVD 88 elevation relationship shown in the table is derived from an average

of several bench mark elevations relative to tide station datum.  As a result of

this averaging, NAVD 88 bench mark elevations computed indirectly from the tidal

datums elevation table may differ slightly from NAVD 88 elevations listed for

each bench mark in the NGS database.