Michael,

There were several notations in the station package that indicates the mark was destroyed, or presumed destroyed  around 1997.  I did find a working benchmark sheet, from 1995, on the 1960 - 1978 epoch that lists the mark.  I believe this is the last time that mark was listed before being dropped from publication.  Benchmark sheet, with datums and elevations below (scroll down for datums and benchmark elevations):

U.S. DEPARTMENT OF COMMERCE

National Oceanic and Atmospheric Administration

National Ocean Service

Station ID: 1611400                                WORKING DATE:      09/12/1995

Name:       NAWILIWILI, NAWILIWILI HARBOR, KAUAI

HAWAII

NOAA Chart: 19383                                  Latitude:         21° 57.4' N

USGS Quad:  LIHUE                                  Longitude:       159° 21.6' W

To reach the tidal bench marks from Lihue Airport, take Ahukini Road (State

Highway 57) to Kapule Highway (State Highway 51), south for 2.4 km (1.5 miles)

to Rice Street, south for 1.3 km (0.8 mile) to Waapa Road, west for 0.3 km (0.2

mile) to the gate for Pier No. 2, and turn south through the gate to the Pier

No. 2 warehouse.  The tide house is located inside the warehouse in the SW

corner.  The bench marks are along the waterfront of Nawiliwili Harbor.

T I D A L   B E N C H   M A R K S

PRIMARY BENCH MARK STAMPING:  NO 14 1974

MONUMENTATION:           Tidal Station disk                        VM#:       13

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete foundation

The bench mark is set in the west entrance to the Pier No. 2 transit shed, 13.1

m (43 ft) south of the NW corner of the warehouse, 0.27 m (0.9 ft) south of the

yellow cone shaped door guard, and 0.40 m (1.3 ft) west of the edge of the

concrete slab.

BENCH MARK STAMPING:  NO 5 1954

MONUMENTATION:           Tidal Station disk                        VM#:        8

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete sidewalk

The bench mark is set in the concrete sidewalk leading to the State of Hawaii

Marine Harbor Patrol Boat Station Pier (former U.S. Coast Guard Boat Station

Pier), 42.1 m (138 ft) south of the wharf face line of Pier 1, 3.05 m (10.0 ft)

west of the west side of the Marine Patrol Building, and 0.15 m (0.5 ft) from

the west end of the sidewalk.

BENCH MARK STAMPING:  NO STAMPING 1

MONUMENTATION:           Tidal Station disk                        VM#:       12

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete filled pipe

The bench mark is a 3/8 inch brass pin set in a 3 inch diameter pipe filled with

concrete (7 inch diameter handhold cover labeled STREET SURVEY MONUMENT) near

the easternmost corner of the wharf face, 52.1 m (171 ft) east of the east end

of the Pier 1 warehouse, 39.3 m (129 ft)  NW of the east end of the east-west

running yellow bulkhead located at the south end of the container yard, and

22.71 m (74.5 ft) NW of the easternmost corner of Pier 1.

BENCH MARK STAMPING:  NO 15 1974

MONUMENTATION:           Tidal Station disk                        VM#:       14

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete apron

The bench mark is set in the concrete apron of Pier No. 1, 9.8 m (32 ft) SE of

the SW corner of the Pier No. 1 transit shed, 2.99 m (9.8 ft) west of the center

of a bollard, 0.27 m (0.9 ft) north of the Pier No. 1 south edge, and 3.66 m

(12.0 ft) east of number 400 on the pier.

BENCH MARK STAMPING:  1400 A 1980

MONUMENTATION:           Tidal Station disk                        VM#:       15

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete foundation

The bench mark is set in the concrete foundation of a bollard, 93.9 m (308 ft)

west of the west end of the Pier No. 2 transit shed, 25.30 m (83.0 ft) NW of the

SW corner of Pier No. 2, 13.1 m (43 ft) west of a light standard on Pier No. 2,

4.12 m (13.5 ft) north of a concrete and rock sea wall, and 0.76 m (2.5 ft) west

of the center of the bollard.

BENCH MARK STAMPING:  1400 B 1980

MONUMENTATION:           Tidal Station disk                        VM#:       16

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete foundation

The bench mark is set in the SW corner of a 0.9 m x 5.2 m (3 ft x 17 ft)

concrete foundation supporting a sugar gantry leading into the Pier No. 2

transit shed, 29.3 m (96 ft) NW of the NW corner of the Pier No. 2 transit shed,

13.7 m (45 ft) NW of the centerline of Waapa Road, and 9.4 m (31 ft) NE of

telephone pole #D90 at the entrance gate to the Shell Oil Company plant.

BENCH MARK STAMPING:  1400 C 1983

MONUMENTATION:           Tidal Station disk                        VM#:       17

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Stainless steel rod

The bench mark is set along the north side of Waapa Road just west of Pier 2,

38.7 m (127 ft) NNW of the sea wall on Nawiliwili Harbor, 17.37 m (57.0 ft) SW

of a yellow fire plug stamped NO 5, 9.30 m (30.5 ft) NW of the centerline of

Waapa Road, 0.61 m (2.0 ft) west of telephone pole #6, and 0.3 m (1 ft) SW of an

orange NGS fiberglass witness post.  The bench mark is crimped to the top of a

9/16 inch diameter stainless steel rod driven 4.3 m (14 ft) to refusal,

protected by a 4 inch diameter PVC pipe projecting 0.10 m (0.2 ft) above grade,

and covered with a threaded PVC pipe cap.

BENCH MARK STAMPING:  1400 D 1983

MONUMENTATION:           Tidal Station disk                        VM#:       18

AGENCY:                                                            PID:   AA3583

SETTING CLASSIFICATION:  Stainless steel rod

The bench mark is set in a park at the junction of State Highway 58 and Waapa

Road, 68.3 m (224 ft) south of the road leading to the seawall, 51.2 m (168 ft)

NW of the navigation range marker located betweeen the two seawalls, 15.85 m

(52.0 ft) west of the west edge of the new seawall, and 0.76 m (2.5 ft) NW of a

1.2 m x 1.2 m x 0.6 m (4 ft x 4 ft x 2 ft) high witness post.  The bench mark is

crimped to the top of a 9/16 inch diameter stainless steel rod driven 4.3 m (14

ft) to refusal, and protected by a 4 inch PVC pipe flush with the natural grade.

BENCH MARK STAMPING:  1400 E 1983

MONUMENTATION:           Tidal Station disk                        VM#:       19

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Stainless steel rod

The bench mark is set in a park at the junction of State Highway 58 and Waapa

Road, 125.3 m (411 ft) south of Bench Mark 1400 D 1983, 121.9 m (400 ft) NE of

Bench Mark NO 5 1954, 91.4 m (300 ft) SSE of a large abandoned cylinder storage

tank, 78.6 m (258 ft) SW of the navigational marker located between the two

seawalls, 11.28 m (37.0 ft) west of the centerline of the paved road adjacent to

the new seawall, and 0.61 m (2.0 ft) west of a 0.6 m (2 ft) high (4 x 4-inch)

witness post.  The bench mark is crimped to the top of a 9/16 inch diameter

stainless steel rod driven 4.3 m (14 ft) to refusal, and protected by a 4 inch

PVC pipe flush with the natural grade.

BENCH MARK STAMPING:  WALL

MONUMENTATION:           Survey disk                               VM#:       21

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete monument

The bench mark is set in a 0.6 m (2 ft) square concrete monument on top of a

seawall running along the north edge of the harbor, 23.01 m (75.5 ft) NW of the

NW corner of a concrete tug boat pier, 6.86 m (22.5 ft) SW of a cyclone fence

bordering the Matson Container Storage area of Pier 2, and 0.15 m (0.5 ft) above

grade.

BENCH MARK STAMPING:  GSL 1400 1988

MONUMENTATION:           Survey disk                               VM#:     6143

AGENCY:                                                            PID:

SETTING CLASSIFICATION:  Concrete foundation

The bench mark is set in the SW corner of a 1.5 m (5 ft) square concrete storm

drain manhole pad, 38.6 m (126 ft) east of the centerline of Waapa road, 12.86 m

(42.2 ft) south of utility pole #2, and 5.88 m (19.3 ft) south of the centerline

of a road leading to the seawall.

T I D A L   D A T U M S

Tidal datums at NAWILIWILI, NAWILIWILI HARBOR, KAUAI based on:

LENGTH OF SERIES:      10 YEARS

TIME PERIOD:           1960-1964 AND 1976-1980

TIDAL EPOCH:           1960-1978

CONTROL TIDE STATION:  1612340 HONOLULU

Elevations of tidal datums referred to Mean Lower Low Water (MLLW), in METERS:

HIGHEST OBSERVED WATER LEVEL (09/10/1981)    =  0.960

MEAN HIGHER HIGH WATER (MHHW)                =  0.567

MEAN HIGH WATER (MHW)                        =  0.427

MEAN SEA LEVEL (MSL)                         =  0.259

MEAN TIDE LEVEL (MTL)                        =  0.247

MEAN LOW WATER (MLW)                         =  0.067

MEAN LOWER LOW WATER (MLLW)                  =  0.000

LOWEST  OBSERVED WATER LEVEL (06/08/1967)    = -0.299

Bench Mark Elevation Information    In METERS above:

Stamping or Designation       MLLW           MHW

NO 14 1974                    2.489         2.062

NO 5 1954                     1.591         1.164

NO STAMPING 1                 2.493         2.067

NO 15 1974                    2.632         2.205

1400 A 1980                   2.447         2.020

1400 B 1980                   2.386         1.959

1400 C 1983                   1.941         1.514

1400 D 1983                   2.200         1.774 = AA3583

1400 E 1983                   1.981         1.554

WALL                          1.900         1.474

GSL 1400 1988                 2.094         1.667

1400 D 1983 = AA3583 = 2.200 - .259 = 1.941 -0.034 sea level rise

from 1960-78 Tidal Epoch to 1983-01 Tidal Epoch = 1.907 m.  The NGS DS circa 1993 shows 1.9m.