Valdez, AK

Post-Flight Aerial Acquisition

Report

October  2012

Contents

1.0 Overview	4

1.1 Vendor Contact Information	4

1.2 Purpose	4

2.0 Acquisition	5

2.1 System Parameters	5

2.2 Base Station Information	5

2.3 Time Period	7

3.0 LiDAR Processing	8

3.1 ABGPS and IMU Processing	8

3.2 Initial LiDAR Processing and Calibration	21

3.3 LiDAR Calibration	23

3.4 LIDAR Processing	23

4.0 Final Accuracy Assessment	24

Appendix A: Condensed Flight Logs	25

M092111A	25

M092611A	26

M092611B	27

M101811A	28

M102811A	29

20120618_180013	30

Tables

1.1 Valdez Project Area	5

2.1 LiDAR System Specifications	5

2.2 Base Station Locations	6

2.3 Acquisition Flight Summary	7

4.1 Internal QC Control Results	24

Figures

1.1 Valdez Coverage Area	4

2.1 Base Station Locations	6

2.2 Flight Line Layout	7

3.1 Separation Plot M092111A	9

3.2 Separation Plot M092611A	9

3.3 Separation Plot M092611B	10

3.4 Separation Plot M101811A	10

3.5 Separation Plot M102811A	11

3.6 Separation Plot 20120618_180013	11

3.7 Altitude Plot M092111A	12

3.8 Altitude Plot M0926111A	12

3.9 Altitude Plot M092611B	13

3.10 Altitude Plot M101811A	13

3.11 Altitude Plot M102811A	14

3.12 Altitude Plot 20120618_180013	14

3.13 PDOPPlot M092111A	15

3.14 PDOP Plot M092611A	15

3.15 PDOP Plot M092611B	16

3.16 PDOP Plot M101811A	16

3.17 PDOP Plot M102811A	17

3.18 PDOP Plot 20120618_180013	17

3.19 Distance from Base Plot M092111A	18

3.20 Distance from Base Plot M092611A	18

3.21 Distance from Base Plot M092611B	19

3.22 Distance from Base Plot M101811A	19

3.23 Distance from Base Plot M102811A	20

3.24 Distance from Base Plot 20120618_180013	20

3.25 POSProc Processing Components	22

3.26 Example Dz Ortho	23

# 1.0 Overview

## 1.1 Vendor Contact Information

## Questions regarding the technical aspects of this report should be addressed to :

AeroMetric, Inc.

Attn:  Jason Mann

2014 Merrill Field Drive

Anchorage, AK 99501

Phone:   907-272-4495

Email:  jmann@aerometric.com

## 1.2 Purpose

Aero-Metric, Inc. acquired highly accurate Light Detection and Ranging (LiDAR) data for an area that consisted of approximately 31 square miles in Valdez, Alaska. This area was a part of the Prince William Sound, Alaska project.  This data was collected for STARR as a part of the FEMA Risk MAP program.  A graphic of the location is provided in Figure 1.1.

The project area was defined in July 2011 in collaboration with FEMA Region X to provide high quality topographic data for two polygons.

Figure 1.1: Valdez Coverage Area

| North | 61° 11’49’’ N | 146° 20’23’’ W |
| --- | --- | --- |
| East | 61° 05’13’’ N | 146° 05’36’’ W |
| South | 61° 04 14’’ N | 1146° 07’56’’ W |
| West | 61° 08’03’’ N | 146°26’18’’ W |

Table 1.1: Valdez Project Extents

# 2.0 Acquisition

## 2.1 System Parameters

LiDAR was collected to the 'Highest' FEMA specification which is equivalent to the 2-foot contour accuracy requirement.  This requires a nominal post spacing of 1 meter.  The LiDAR system parameters to meet this requirement are found in Table 2.1.

| Aircraft | Piper Navajo N812T and Piper Navajo N6GR |
| --- | --- |
| Flying Height (AGL) | 1700 meters |
| Laser Pulse Rate | 70 kHz |
| Mirror Scan Frequency | 70 Hz |
| Scan Angle | (+/-) 10o |
| Side Lap | 67% |
| Number of Flight Lines | 120 |
| Flight Line Spacing | 304.98 meters |
| Flight Line Coverage | 64.74 sq. km. |
| Ground Speed | 140 - 160 knots |
| Nominal Point Density | 8 points per square meter per pass |
| Datums | NAD83 |
|  | NAVD88 via Geoid09 (feet) |
| Projection | Universal Transverse Mercator (UTM) Zone 6N |

Table 2.1 LiDAR System Specifications

## 2.2 Base Station Information

Base Station Information: All missions were processed using base stations located at the Valdez airport.. Table 2.2  and Figure 2.1 provide the base station location information..

| POINT | LAT | LONG | HEIGHT (Ellipsoid) |
| --- | --- | --- | --- |
| 45652650 | 61°07’55.74551” | 146°14’18.26593” | 44.372m |
| 83682650 | 61°07’55.88430” | 146°14’16.92884” | 44.663m |
| 19112910 | 61°07’55.88496” | 146°14’16.93058” | 44.661m |
| 45652910 | 61°07’55.74544” | 146°14’18.26743” | 44.389m |

Table 2.2: Base Station Location

## Figure 2.1: Base Station Location

## 2.3 Time Period

LiDAR data acquisition for the project had to be collected at two different times. First was collected between September 21, 2011 and October 28, 2011 in total of five (5) flight missions.  A second collection was need to fill in the middle of the project area and (1) one mission was collected on June 18, 2012.

| Acquisition Date | Mission | Time | Lines Acquired |
| --- | --- | --- | --- |
| 20110921 | M092111A | 00:55-02:55 UTM | lines 19-36 |
| 20110926 | M092611A | 18:40-21:07 UTM | lines 97-120 |
| 20110926 | M092611B | 23:45-03:12 UTM | lines 1-18, 70,78-96 |
| 20111018 | M101811A | 18:47-21:49 UTM | lines 37-61 |
| 20111028 | M102811A | 20:29-23:01 UTM | lines 44-59, 35-37, 77 |
| 20120618 | 120618_180013 | 18:04-19: UTM | lines 1-13 |

Table 2.3: Acquisition Flight Summary

Figure 2.2: Flight Line Layout

# 3.0 LiDAR Processing

## 3.1 ABGPS and IMU Processing

Applanix - POSGNSS

Utilizing carrier phase ambiguity resolution on the fly (i.e., without initialization),  the solution to sub-decimeter kinematic positioning without the operational constraint of static initialization as used in semi-kinematic or stop-and-go positioning was utilized for the airborne GNSS post-processing.

The processing technique used by Applanix, Inc. for achieving the desired accuracy is Kinematic Ambiguity Resolution (KAR).  KAR searches for ambiguities and uses a special method to evaluate the relative quality of each intersection (RMS).  The quality indicator is used to evaluate the accuracy of the solution for each processing computation.  In addition to the quality indicator, the software will compute separation plots between any two solutions, which will ultimately determine the acceptance of the airborne GNSS post processing.

Inertial Data

The post-processing of inertial and aiding sensor data (i.e. airborne GNSS post processed data) is to compute an optimally blended navigation solution. The Kalman filter-based aided inertial navigation algorithm generates an accurate (in the sense of least-square error) navigation solution that will retain the best characteristics of the processed input data.  An example of inertial/GNSS sensor blending is the following: inertial data is smooth in the short term.  However, a free-inertial navigation solution has errors that grow without bound with time.  A GNSS navigation solution exhibits short-term noise but has errors that are bounded.  This optimally blended navigation solution will retain the best features of both, i.e. the blended navigation solution has errors that are smooth and bounded.

The resultant processing generates the following data:

- Position:		Latitude, Longitude, Altitude

- Velocity:	North, East, and Down components

- 3-axis attitude:	roll, pitch, true heading

- Acceleration:	x, y, z components

- Angular rates:	x, y, z components

GPS Separation Plots

Figure 3.1: Separation Plot M092111A

Figure 3.2:  Separation Plot M092611A

Figure 3.3: Separation Plot M092611B

Figure 3.4: Separation Plot M101811A

Figure 3.5:  Separation Plot M102811A

Figure 3.6: Separation Plot 120618_180013

GPS Altitude Plots

Figure 3.7: Altitude Plot M092111A

Figure 3.8: Altitude Plot M092611A

Figure 3.9: Altitude Plot M092611B

Figure 3.10: Altitude Plot M101811A

Figure 3.11: Altitude Plot M102811A

Figure 3.12: Altitude Plot 120618_180013

GPS PDOP Plots

Figure 3.13: PDOP Plot M092111A

Figure 3.14: PDOP Plot M092611A

Figure 3.15: PDOP Plot M092611B

Figure 3.16: PDOP Plot M101811A

Figure 3.17: PDOP Plot M102811A

Figure 3.18: PDOP Plot 120618_180013

Distance from Base Plots

Figure 3.19: Distance from Base Plot M092111A

Figure3.20: Distance from Base Plot M092611A

Figure3.21: Distance from Base Plot M092611B

Figure3.22: Distance from Base Plot M101811A

Figure3.23: Distance from Base Plot M102811A

Figure3.24: Distance from Base Plot 20120618_180013

## 3.2 Initial LiDAR Processing and Calibration

The airborne GPS and blending of inertial and GPS post-processing were completed in multiple steps.

- The collected data was transferred from the field data collectors to the main computer.  Data was saved under the project number and separated between LiDAR mission dates.  Inside each mission date, a sub-directory was created with the aircraft’s tail number and an A or B suffix was attached to record which mission of the day the data is associated with.  Inside the tail number sub-directory, five sub-directories were also created: EO, GPS, IMU, PROC, and RAW.

- The aircraft raw data (IMU and GPS data combined) was run through a data extractor program.  This separated the IMU and GPS data.  In addition to the extraction of data, it provided the analyst the first statistics on the overall flight.  The program was POSPac (POS post-processing PACkage).

- Executing POSGPS program to derive accurate GPS positions for all flights:

Applanix POSGPS

The software utilized for the data collected was PosGPS, a kinematic on-the-fly (OTF) processing software package. Post processing of the data is computed from each base station (Note: only base stations within the flying area were used) in both a forward and backward direction. This provides the analyst the ability to Quality Check (QC) the post processing, since different ambiguities are determined from different base stations and also with the same data from different directions.

The trajectory separation program is designed to display the time of week that the airborne or roving antenna traveled, and compute the differences found between processing runs.  Processed data can be compared between a forward/reverse solution from one base station, a reverse solution from one base station and a forward solution from the second base station, etc.  For the Applanix POSGPS processing, this is considered the final QC check for the given mission.  If wrong ambiguities were found with one or both runs, the analyst would see disagreements from the trajectory plot, and re-processing would continue until an agreement was determined.

Once the analyst accepts a forward and reverse processing solution, the trajectory plot is analyzed and the combined solution is stored in a file format acceptable for the IMU post processor.

- When the processed trajectory (either through POSGPS) data was accepted after quality control analysis, the combined solution is stored in a file format acceptable for the IMU post processor (i.e. POSProc).

- Execute POSProc.

POSProc comprises a set of individual processing interface tools that execute and provide the following functions:

Figure 3.25: POSProc Processing Components

Integrated Inertial Navigation (iin) Module.

The name iin is a contraction of Integrated Inertial Navigation.  iin reads inertial data and aiding data from data files specified in a processing environment file and computes the aided inertial navigation solution.  The inertial data comes from a strapdown IMU.  iin outputs the navigation data between start and end times at a data rate as specified in the environment file.  iin also outputs Kalman filter data for analysis of estimation error statistics and smoother data that the smoothing program smth uses to improve the navigation solution accuracy.

iin implements a full strapdown inertial navigator that solves Newton’s equation of motion on the earth using inertial data from a strapdown IMU.  The inertial navigator implements coning and sculling compensation to handle potential problems caused by vibration of the IMU.

Smoother Module (smth)

smth is a companion processing module to iin.  smth is comprised of two individual functions that run in sequence.  smth first runs the smoother function and then runs the navigation correction function.

The smth smoother function performs backwards-in-time processing of the forwards-in-time blended navigation solution and Kalman filter data generated by iin to compute smoothed error estimates.  smth implements a modified Bryson-Frazier smoothing algorithm specifically designed for use with the iin Kalman filter.  The resulting smoothed strapdown navigator error estimates at a given time point are the optimal estimates based on all input data before and after the given time point.  In this sense, smth makes use of all available information in the input data.  smth writes the smoothed error estimates and their RMS estimation errors to output data files.

The smth navigation correction function implements a feedforward error correction mechanism similar to that in the iin strapdown navigation solution using the smoothed strapdown navigation errors.  smth reads in the smoothed error estimates and with these, corrects the strapdown navigation data.  The resulting navigation solution is called a Best Estimate of Trajectory (BET), and is the best obtainable estimate of vehicle trajectory with the available inertial and aiding sensor data.

The above mentioned modules provide the analyst the following statistics to ensure that the most optimal solution was achieved: a log of the iin processing, the Kalman filter Measurement Residuals, Smoothed RMS Estimation Errors, and Smoothed Sensor Errors and RMS.

## 3.3 LiDAR Calibration

The purpose of the LiDAR system calibration is to refine the system parameters in order for the post-processing software to produce a “point cloud” that best fits the actual ground.

For each mission, LiDAR data for at least one cross flight is acquired over the mission’s acquisition site.  The processed data of the cross flight is compared to the perpendicular flight lines using either the Optech proprietary software or TerraSolid's TerraMatch software to determine if any systematic errors are present.  In this calibration, the data of individual flight lines are compared against each other and their systematic errors are corrected in the final processed data.

## 3.4 LIDAR Processing

The LAS files were then imported, verified, and parsed into manageable, tiled grids using GeoCue.

After the data has been processed and calibrated a relative accuracy assessment is performed comparing flightline to flightline for proper position between flightlines. A data density test is also performed to ensure proper coverage. Aerometric uses GeoCue to create ortho images by elevation differences.  The generated orthos have assigned elevation ranges that allow the technician to evaluate if the data passes the accuracy assessment and determine if additional calibration efforts are needed based on the bias trends.  In Section 4, Figures 4-1 represent an example of  the elevation orthos comparing  neighboring flightline vertical positions. Green indicates a difference of less than 5cm; yellow is 5cm to 10cm; orange is 10cm to 15cm; and red is greater than 15cm.  Areas containing dense vegetation coverage, or inundation from water will show as having higher elevation miss-match then is actually present in the ground data.  This is because these regions have more point returns off objects and fewer returns from the ground making the miss match appear greater than it actually is.

Figure 3.26: Example Dz Ortho

# 4.0 Final Accuracy Assessment

Data Verification:

The data was verified using the ground control data collected by Compass Data, Inc. 20 points were distributed throughout the project area and the points were compared to the LIDAR data using TerraScan. TerraScan computes the vertical differences between the surveyed elevation and the LiDAR derived elevation for each point.

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

VAL101            547757.901  6771608.312    47.119    47.120    +0.001

VAL102            544527.346  6772495.157     8.491     8.570    +0.079

VAL103            543262.869  6773688.693    11.173    11.210    +0.037

VAL104            541867.525  6774337.270    10.538    10.490    -0.048

VAL105            542719.894  6777438.450    44.301    44.180    -0.121

VAL106            543689.812  6779111.216    72.300    72.360    +0.060

VAL107            540647.928  6776979.030    19.599    19.610    +0.011

VAL108            542321.641  6775040.070    16.412    16.420    +0.008

VAL109            539068.067  6776503.740     5.148     5.250    +0.102

VAL110            538229.178  6777412.460     4.999     5.000    +0.001

VAL111            537891.320  6777174.518     6.693     6.730    +0.037

VAL112            535975.746  6778375.971     5.724     5.830    +0.106

VAL113            534482.948  6776945.499     6.630     6.560    -0.070

VAL114            534461.085  6778212.145    16.968    16.980    +0.012

VAL115            534329.534  6780948.380    65.947    65.970    +0.023

VAL116            532150.658  6777732.386     5.883     5.850    -0.033

VAL117            532954.160  6778185.267    14.351    14.390    +0.039

VAL118            534130.630  6779266.061    48.005    48.080    +0.075

VAL119            534742.330  6782737.864    88.393    88.340    -0.053

VAL120            535615.081  6784561.818   139.320   139.300    -0.020

Average dz           +0.012

Minimum dz           -0.121

Maximum dz           +0.106

Average magnitude     0.047

Root mean square      0.058

Std deviation         0.059

Table 4.1: Internal QC Control Results

# Appendix A: Condensed Flight Logs

## M092111A

## M092611A

## M092611B

## M101811A

## M102811A

## 20120618_180013