Elevation QA Report

Project:       Contractor:

Data Delivery Date:   Date Data Reviewed:

Reviewer:    Total Square Miles Reviewed:

Elevation Type:     Format:       Grid Spacing:    Tile size:

Projection:       Zone:       Datum:         Units:

Licensing:           Metadata:

Materials Received:

Vertical Accuracy Test Performed:       Test Point Source:            RMSE:

Vertical Accuracy Test Notes:

QC Review Summary:

11-2-2010

LiDAR Quality Control (QC) Review Process

Preparation:

-Metadata reviewed to determine data projection, datum, format, etc.

-If ARRA contract, check for raw .LAS files, classified .LAS files, breaklines, blind control points,

and DEM in Image or Grid format

-Open data in Global Mapper

Vertical accuracy testing:

-If ARRA contract, use Vertical Accuracy Test Worksheet to perform RMSE on 20 blind point

positions provided by contractor

Inspection and Correction of data:

-Minimum and maximum elevations in dataset; correct if in error

-Appropriate hydro flattening as specified in V12 Lidar Specification (For ARRA/GPSC Data)

-Data void areas

-Data spikes

-Tile edge seam lines

-Non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Elevation errors - raised/lowered areas/tiles

-Other surface treatment anomalies

-Check DRGs for correct elevations and horizontal positioning (if test points not available)

-Create footprint (project boundary) shape file and establish square miles

During Inspection, identify data errors and create “error” file folder:

-Capture geo-referenced JPG or TIFF image(s) of identified errors

-Copy to Error file

During Inspection, level elevations and remove artifacts (these two steps not done for ARRA data):

-Level smoothing to remove non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Level data spikes where possible

Export image files and create project Elevation QC Review Report:

-Export ERDAS Imagine image files in native projection and resolution

-If ARRA, Copy Vertical Accuracy Test Worksheet into QC Report

-Place QC Review Process and Project Area Extent into QC Report

-If rejected, attach sample geo-referenced JPG or TIFF error images with an explanation of reason

-If rejected, restart QC process when replacement data is received

-Provide completed Elevation QC Review Report to Elevation Supervisor for final viewing

-Add QC Report, footprint, Imagine image(s), and Error file to original data file for final shipment to EROS

Baldwin Co. West AL Area Extent

Vertical Accuracy

| Baldwin Co. AL East-West- Vertical Accuracy Statistic Worksheet |  |  |  |
| --- | --- | --- | --- |
| elevations units in meters |  |  |  |
| A | D | E | F | G | H |  |
| Point | Point | z | z |  |  |  |
| number | description | Vendor Elev | NGTOC Elev | diff in z | (diff in z)2 | Comments |
| B101 | B101 | 1.355 | 1.322 | 0.033 | 0.001 |  |
| B102 | B102 | 5.689 | 5.624 | 0.065 | 0.004 |  |
| B103 | B103 | 19.822 | 19.786 | 0.036 | 0.001 |  |
| B104 | B104 | 14.042 | 14.04 | 0.002 | 0.000 |  |
| B105 | B105 | 1.851 | 1.964 | -0.113 | 0.013 |  |
| B201 | B201 | 12.917 | 12.428 | 0.489 | 0.239 |  |
| B202 | B202 | 20.79 | 20.73 | 0.060 | 0.004 |  |
| B203 | B203 | 9.783 | 9.803 | -0.020 | 0.000 |  |
| B204 | B204 | 23.311 | 23.369 | -0.058 | 0.003 |  |
| B205 | B205 | 22.356 | 22.41 | -0.054 | 0.003 |  |
| B206 | B206 | 25.102 | 25.021 | 0.081 | 0.007 |  |
| B207 | B207 | 1.13 | 1.027 | 0.103 | 0.011 |  |
| B208 | B208 | 15.603 | 15.568 | 0.035 | 0.001 |  |
| B209 | B209 | 27.88 | 27.927 | -0.047 | 0.002 |  |
| B210 | B210 | 3.961 | 3.995 | -0.034 | 0.001 |  |
| B211 | B211 | 22.755 | 22.715 | 0.040 | 0.002 |  |
| B212 | B212 | 11.827 | 11.862 | -0.035 | 0.001 |  |
| B213 | B213 | 25.704 | 25.67 | 0.034 | 0.001 |  |
| B214 | B214 | 22.613 | 22.59 | 0.023 | 0.001 |  |
| B215 | B215 | 57.755 | 57.734 | 0.021 | 0.000 |  |
| B216 | B216 | 38.235 | 38.175 | 0.060 | 0.004 |  |
| Outlier: a control point located in an area that does not reflect the true ground elevation, i.e. bridges, etc. | average | 0.000 |  |
|  | RMSEz | 0.013 | 1.3cm |
|  | NSSDA | 0.026 |  |